## Slide 1
程序的机器级表示(6)
王晶
jwang@ruc.edu.cn，信息楼124
2023年11月

## Slide 2: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 3: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 4: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 5: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 6: Callee-Saved Example #1
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
x comes in register %rdi.
We need %rdi for the call to incr.
Where should be put x, so we can use it after the call to incr?

## Slide 7: Callee-Saved Example #2
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
%rsp
Resulting Stack Structure
. . .
Rtn address
Saved %rbx
Notes: We are a callee, must save %rbx (to stack)

## Slide 8: Callee-Saved Example #3
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
Initial Stack Structure
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
%rsp
. . .
Rtn address
Saved %rbx

## Slide 9: Callee-Saved Example #4
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
x is saved in %rbx, a callee saved register
Notes: Rdi is x;

## Slide 10: Callee-Saved Example #5
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
x is saved in %rbx, a callee saved register

## Slide 11: Callee-Saved Example #6
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
Upon return from incr:
x safe in %rbx
Return val v2 in %rax
Compute x+v2: addq %rbx, %rax
Notes: If incr() used rbx, it had to restore call_incr2()’s rbx value before returning

## Slide 12: Callee-Saved Example #7
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
Saved %rbx
Return result in %rax

## Slide 13: Callee-Saved Example #8
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Initial Stack Structure
. . .
Rtn address
Saved %rbx
18213
Unused
%rsp
. . .
Rtn address
Saved %rbx
final Stack Structure
Remember: we saved %rbx onto stack earlier. Need to restore.
Notes: Remember: we saved %rbx onto stack earlier. Need to restore.

## Slide 14: Example
1 int swap_add(int *xp, int *yp)
2 {
3 int x = *xp;
4 int y = *yp;
5
6 *xp = y;
7 *yp = x;
8 return x + y;
9 }
10

## Slide 15: Example
11 int caller()
12 {
13 int arg1 = 534;
14 int arg2 = 1057;
15 int sum = swap_add(&arg1, &arg2);
16 int diff = arg1 - arg2;
17
18 return sum * diff;
19 }

## Slide 16: Example
0 | Saved %ebp
-4 | 1057(arg2)
-8 | 534(arg1)
-12 | 
Stack frame for caller
Before
int sum = swap_add(&arg1, &arg2);
%ebp
%esp

## Slide 17: Parameter Passing
0 | Saved %ebp
-4 | 1057(arg2)
-8 | 534(arg1)
-12 | &arg2
Stack frame for caller
1 leal -4(%ebp),%eax
Compute &arg2
2 pushl %eax
Push &arg2
%ebp
%esp

## Slide 18: Parameter Passing
0 | Saved %ebp
-4 | 1057(arg2)
-8 | 534(arg1)
-12 | &arg2
-16 | &arg1
Stack frame for caller
1 leal -4(%ebp),%eax
Compute &arg2
2 pushl %eax
Push &arg2
3 leal -8(%ebp),%eax
Compute &arg1
4 pushl %eax
Push &arg1
%ebp
%esp

## Slide 19: Call Instruction
0 | Saved %ebp
-4 | 1057(arg2)
-8 | 534(arg1)
-12 | &arg2
-16 | &arg1
-20 | Return Addr
Stack frame for caller
1 leal -4(%ebp),%eax
Compute &arg2
2 pushl %eax
Push &arg2
3 leal -8(%ebp),%eax
Compute &arg1
4 pushl %eax
Push &arg1
5 call swap_add
Call the swap_add function
%ebp
%esp

## Slide 20: Setup code in swap_add
0 | Saved %ebp
-4 | 1057(arg2)
-8 | 534(arg1)
-12 | yp(&arg2)
-16 | xp(&arg1)
-20 | Return Addr
-24 | Saved %ebp
Stack frame for caller
swap_add:
1 pushl %ebp Save old %ebp
%ebp
%esp

## Slide 21: Setup code in swap_add
24 | Saved %ebp
20 | 1057(arg2)
16 | 534(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
Stack frame for caller
swap_add:
1 pushl %ebp Save old %ebp
2 movl %esp,%ebp
Set %ebp as frame pointer
%ebp
%esp
Stack frame for swap_add

## Slide 22: Setup code in swap_add
24 | Saved %ebp
20 | 1057(arg2)
16 | 534(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
swap_add:
1 pushl %ebp Save old %ebp
2 movl %esp,%ebp
Set %ebp as frame pointer
3 pushl %ebx
Save %ebx
%esp
%ebp
Stack frame for swap_add

## Slide 23: Body code in swap_add
24 | Saved %ebp
20 | 1057(arg2)
16 | 534(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
5 movl 8(%ebp),%edx Get xp

## Slide 24: Body code in swap_add
24 | Saved %ebp
20 | 1057(arg2)
16 | 534(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
5 movl 8(%ebp),%edx Get xp
6 movl 12(%ebp),%ecx Get yp

## Slide 25: Body code in swap_add
24 | Saved %ebp
20 | 1057(arg2)
16 | 534(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
5 movl 8(%ebp),%edx Get xp
6 movl 12(%ebp),%ecx Get yp
7 movl (%edx),%ebx Get x
8 movl (%ecx),%eax Get y
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
534
%ebx
1057
%eax

## Slide 26: Body code in swap_add
24 | Saved %ebp
20 | 1057(arg2)
16 | 1057(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
9 movl %eax, (%edx) Store y at *xp
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
534
%ebx
1057
%eax

## Slide 27: Body code in swap_add
24 | Saved %ebp
20 | 534(arg2)
16 | 1057(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
9 movl %eax, (%edx) Store y at *xp
10 movl %ebx, (%ecx) Store x at *yp
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
534
%ebx
1057
%eax

## Slide 28: Body code in swap_add
24 | Saved %ebp
20 | 534(arg2)
16 | 1057(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
9 movl %eax, (%edx) Store y at *xp
10 movl %ebx, (%ecx) Store x at *yp
11 addl %ebx,%eax Set return value = x+y
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
534
%ebx
1591
%eax

## Slide 29: Finishing code in swap_add
24 | Saved %ebp
20 | 534(arg2)
16 | 1057(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
12 popl %ebx Restore %ebx
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
original value
%ebx
1591
%eax

## Slide 30: Finishing code in swap_add
24 | Saved %ebp
20 | 534(arg2)
16 | 1057(arg1)
12 | yp(&arg2)
8 | xp(&arg1)
4 | Return Addr
0 | Saved %ebp
-4 | Saved %ebx
Stack frame for caller
12 popl %ebx Restore %ebx
13 movl %ebp, %esp Restore %esp
%esp
%ebp
Stack frame for swap_add
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
original value
%ebx
1591
%eax

## Slide 31: Finishing code in swap_add
0 | Saved %ebp
-4 | 534(arg2)
-8 | 1057(arg1)
-12 | yp(&arg2)
-16 | xp(&arg1)
-20 | Return Addr
 | Saved %ebp
 | Saved %ebx
Stack frame for caller
12 popl %ebx Restore %ebx
13 movl %ebp, %esp Restore %esp
14 popl %ebp Restore %ebp
%ebp
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
original value
%ebx
1591
%eax
%esp

## Slide 32: Finishing code in swap_add
0 | Saved %ebp
-4 | 534(arg2)
-8 | 1057(arg1)
-12 | yp(&arg2)
-16 | xp(&arg1)
-20 | Return Addr
 | Saved %ebp
 | Saved %ebx
Stack frame for caller
12 popl %ebx Restore %ebx
13 movl %ebp, %esp Restore %esp
14 popl %ebp Restore %ebp
15 ret Return to caller
Call by value
%ebp
xp(=&arg1=%ebp+16)
%edx
yp(=&arg2=%ebp+20)
%ecx
original value
%ebx
1591
%eax
%esp

## Slide 33
int proc(void) {
int x, y;
scanf(“%x %x”, &y, &x);
return x-y;
}
过程proc开始时，esp值为0x800040, ebp值为0x00060，scanf输入值为0x46和0x53, “%x %x”地址为0x300070.
第3行ebp的值被设为多少？
第4行esp的值被设为多少？
局部变量x和y的地址是多少？
画出scanf返回后的栈图
指出proc函数未使用的栈区的地址
GCC产生如下汇编代码
proc
Pushl %ebp
Movl %esp, %ebp
Subl $40, %esp
Leal -4(%ebp), %eax
Movl %eax, 8(%esp)
Leal -8(%ebp), %eax
Movl %eax, 4(%esp)
Movl $.LCO, (%esp);常量字符串“%x %x”的地址
Call scanf
Movl -4(%ebp), %eax
Subl -8(%ebp), %eax
Movl %ebp, %esp,
Popl %ebp
Ret
Notes: A. 0x80003c; B. 0x800014; C. x:0x800038, y: 0x800034; E. 0x800020~0x800033

## Slide 34
int proc(void) {
int x, y;
scanf(“%x %x”, &y, &x);
return x-y;
}
过程proc开始时，esp值为0x800040, ebp值为0x00060，scanf输入值为0x46和0x53, “%x %x”地址为0x300070.
第3行ebp的值被设为多少？
第4行esp的值被设为多少？
局部变量x和y的地址是多少？
画出scanf返回后的栈图
指出proc函数未使用的栈区的地址
GCC产生如下汇编代码
proc
Pushl %ebp
Movl %esp, %ebp
Subl $40, %esp
Leal -4(%ebp), %eax
Movl %eax, 8(%esp)
Leal -8(%ebp), %eax
Movl %eax, 4(%esp)
Movl $.LCO, (%esp);常量字符串“%x %x”的地址
Call scanf
Movl -4(%ebp), %eax
Subl -8(%ebp), %eax
Movl %ebp, %esp,
Popl %ebp
Ret
0x80003c;
0x800014;
x:0x800038, y: 0x800034;
0x800020~0x800033
Notes: A. 0x80003c; B. 0x800014; C. x:0x800038, y: 0x800034; E. 0x800020~0x800033

## Slide 35: Recursive Function
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Notes: rep; ret: AMD的分支预测器中存在一个问题，即单字节ret紧跟在您引用的代码（以及其他一些情况）中的条件跳转之后，并且解决方法是添加rep前缀，CPU会忽略该前缀，但是修正预测变量。

## Slide 36: Recursive Function Terminal Case
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rax | Return value | Return value

## Slide 37: Recursive Function Register Save
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rsp
. . .
Rtn address
Saved %rbx

## Slide 38: Recursive Function Call Setup
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x >> 1 | Rec. argument
%rbx | x & 1 | Callee-saved

## Slide 39: Recursive Function Call
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Recursive call return value | 

## Slide 40: Recursive Function Result
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Return value | 

## Slide 41: Recursive Function Completion
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rax | Return value | Return value
%rsp
. . .
Notes: 在两种条件下无法发挥cpu的分支预测功能： 1> 一个分支，里面带有near-return（opcode C3h），例如 label： ret 2> 一个判断条件紧跟着就是near-return，例如 jle label2 ret
为了使得代码还是能够用得上cpu的分支预测（branch prediction），最简单的解决办法就是在ret前面插入rep，这称之为two-byte ret，使得性能可以提高。

## Slide 42: 课堂练习
一个具有通用结构的C函数如下：
long rfun (unsigned long x) {
if ( ______________ )
return ___________;
unsigned long nx =________;
long rv = rfun(nx);
return _____________;
}
请填写C语言代码中缺失的表达式；rfun存储在被调用者保存寄存器%rbx中的值是_________。
GCC产生的汇编代码如下：
long rfun (unsigned long x)
x in %rdi
rfun:
pushq %rbx
movq %rdi, %rbx
movl $0, %eax
testq %rdi, %rdi
je .L2
shrq $2, $rdi
call rfun
addq %rbx, %rax
.L2
popq %rbx
ret
Notes: If (X == 0) return 0;
Unsigned long nx = x/4
Long rv = rfun(nx);
Return rv+x;
%rbx中的值是传入函数的参数x

## Slide 43: 课堂练习
一个具有通用结构的C函数如下：
long rfun (unsigned long x) {
if ( ______________ )
return ___________;
unsigned long nx =________;
long rv = rfun(nx);
return _____________;
}
请填写C语言代码中缺失的表达式；rfun存储在被调用者保存寄存器%rbx中的值是_________。
GCC产生的汇编代码如下：
long rfun (unsigned long x)
x in %rdi
rfun:
pushq %rbx
movq %rdi, %rbx
movl $0, %eax
testq %rdi, %rdi
je .L2
shrq $2, $rdi
call rfun
addq %rbx, %rax
.L2
popq %rbx
ret
x == 0
x 或者 0
x /4
rv+x
Notes: If (X == 0) return 0;
Unsigned long nx = x/4
Long rv = rfun(nx);
Return rv+x;
%rbx中的值是传入函数的参数x

## Slide 44: 课堂练习
程序填空，变量映射关系，并解释函数功能
Int fun_a(unsigned x) {
int val = 0;
while ( x ) {
val ^= x;
x>>=1
}
return val&0x01;
}
x@$ebp+8
Movl 8(%ebp), %edx
Movl $0, %eax
Testl %edx, %edx
Je .L7
.L10:
xorl %edx, %eax
shrl %edx ;逻辑右移1位
jne .L10
.L7:
andl $1, %eax

## Slide 45: 课堂练习
程序填空，变量映射关系，并解释函数功能
Int fun_a(unsigned x) {
int val = 0;
while ( x ) {
val ^= x;
x>>=1
}
return val&0x01;
}
x@$ebp+8
Movl 8(%ebp), %edx
Movl $0, %eax
Testl %edx, %edx
Je .L7
.L10:
xorl %edx, %eax
shrl %edx ;逻辑右移1位
jne .L10
.L7:
andl $1, %eax

## Slide 46: 课堂练习
函数fun_b(unsigned long x) {
  Long val = 0;
  Long i;
  For (… ; … ; …) {
    …
  }
  Return val;
}
Gcc生成的汇编代码如右所示。
完成下面工作：
  A. 根据汇编代码，填写C代码缺失的部分；
  B. 解释循环前为什么没有初始测试，也没有初始跳转到循环内部的测试部分；
  C. 用自然语言描述这个函数的功能
# x in %rdi
1 func_b:
Movl $64, %edx
movl $0, %eax
.L10:
movq %rdi, %rcx
andl $1, %ecx
addq %rax, %rax
orq % rcx, %rax
shrq %rdi
subq $1, %rdx
jne .L10
ret

## Slide 47: 练习答案
fun_b(unsigned long x) {
  Long val = 0;
  Long i;
  For (i=64; i!=0 ; i--) { // 尽量忠于原意
    Val = (val << 1) | (x&1)
    X >>= 1;
  }
  Return val;
}
2）因为循环次数是常量
3）将x镜像反转

## Slide 48: Observations About Recursion
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
    Unless the C code explicitly does so (e.g., buffer overflow in Lecture 9)
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 49: x86-64 Procedure Summary
Important Points
  Stack is the right data structure for procedure call / return
    If P calls Q, then Q returns before P
Recursion (& mutual recursion) handled by normal calling conventions
  Can safely store values in local stack frame and in callee-saved registers
  Put function arguments at top of stack
  Result return in %rax
Pointers are addresses of values
  On stack or global
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %rbp
Arguments
7+
Caller
Frame
%rbp
(Optional)
%rsp

## Slide 50: Today
Arrays
  One-dimensional
  Multi-dimensional (nested)
  Multi-level
Structures
  Allocation
  Access
  Alignment
Floating Point

## Slide 51: Array Allocation
Basic Principle
  T A[L];
  Array of data type T and length L
  Contiguously allocated region of L * sizeof(T) bytes in memory
char string[12];
x
x + 12
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20
double a[3];
x + 24
x
x + 8
x + 16
char *p[3];
x
x + 8
x + 16
x + 24

## Slide 52: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0: Type T*
Reference Type Value
  val[4] int
  val int *
  val+1 int *
  &val[2] int *
  val[5] int
  *(val+1) int
  val + i int *
int val[5];
1
5
2
1
3
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 53: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0: Type T*
Reference Type Value
  val[4] int 3
  val int *
  val+1 int *
  &val[2] int *
  val[5] int
  *(val+1) int
  val + i int *
int val[5];
1
5
2
1
3
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 54: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0: Type T*
Reference Type Value
  val[4] int 3
  val int * x
  val+1 int * x + 4
  &val[2] int * x + 8
  val[5] int ??
  *(val+1) int 5 //val[1]
  val + i int * x + 4 * i //&val[i]
int val[5];
1
5
2
1
3
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 55: Array Example
Declaration “zip_dig cmu” equivalent to “int cmu[5]”
Example arrays were allocated in successive 20 byte blocks
  Not guaranteed to happen in general
#define ZLEN 5
typedef int zip_dig[ZLEN];
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig ucb = { 9, 4, 7, 2, 0 };
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig ucb;
9
4
7
2
0
56
60
64
68
72
76

## Slide 56: Array Accessing Example
Register %rdi contains starting address of array
Register %rsi contains array index
Desired digit at %rdi + 4*%rsi
Use memory reference (%rdi,%rsi,4)
int get_digit
(zip_dig z, int digit)
{
return z[digit];
}
# %rdi = z
# %rsi = digit
movl (%rdi,%rsi,4), %eax # z[digit]
IA32
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36

## Slide 57: Array Loop Example
# %rdi = z
movl $0, %eax # i = 0
jmp .L3 # goto middle
.L4: # loop:
addl $1, (%rdi,%rax,4) # z[i]++
addq $1, %rax # i++
.L3: # middle
cmpq $4, %rax # i:4
jbe .L4 # if <=, goto loop
rep; ret
void zincr(zip_dig z) {
size_t i;
for (i = 0; i < ZLEN; i++)
z[i]++;
}

## Slide 58: Multidimensional (Nested) Arrays
Declaration
  T A[R][C];
  2D array of data type T
  R rows, C columns
  Type T element requires K bytes
Array Size
  R * C * K bytes
Arrangement
  Row-Major Ordering
A[0][0]
A[0][C-1]
A[R-1][0]
• • •
• • •
A[R-1][C-1]
•
•
•
•
•
•
int A[R][C];
• • •
A
[0]
[0]
A
[0]
[C-1]
• • •
A
[1]
[0]
A
[1]
[C-1]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
4*R*C Bytes
Notes: Board: show 3D example: a[2][3][2] to illustrate the idea of row major as enumerating indices from right to left

## Slide 59: Nested Array Example
“zip_dig pgh[4]” equivalent to “int pgh[4][5]”
  Variable pgh: array of 4 elements, allocated contiguously
  Each element is an array of 5 int’s, allocated contiguously
“Row-Major” ordering of all elements in memory
#define PCOUNT 4
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
zip_dig
pgh[4];
76
96
116
136
156
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1

## Slide 60: Nested Array Row Access
• • •
Row Vectors
  A[i] is array of C elements
  Each element of type T requires K bytes
  Starting address A + i * (C * K)
• • •
A
[i]
[0]
A
[i]
[C-1]
A[i]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
A[R-1]
• • •
A
• • •
A
[0]
[0]
A
[0]
[C-1]
A[0]
A+(i*C*4)
A+((R-1)*C*4)
int A[R][C];

## Slide 61: Nested Array Row Access Code
Row Vector
  pgh[index] is array of 5 int’s
  Starting address pgh+20*index
Machine Code
  Computes and returns address
  Compute as pgh + 4*(index+4*index)
int *get_pgh_zip(int index)
{
return pgh[index];
}
# %rdi = index
leaq (%rdi,%rdi,4),%rax # 5 * index
leaq pgh(,%rax,4),%rax # pgh + (20 * index)
pgh
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
pgh[2]

## Slide 62: Nested Array Element Access
• • •
Array Elements
  A[i][j] is element of type T, which requires K bytes
  Address A + i * (C * K) + j * K = A + (i * C + j)* K
• • • • • •
A
[i]
[j]
A[i]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
A[R-1]
• • •
A
• • •
A
[0]
[0]
A
[0]
[C-1]
A[0]
A+(i*C*4)
A+((R-1)*C*4)
int A[R][C];
A+(i*C*4)+(j*4)

## Slide 63: Nested Array Element Access Code
Array Elements
  pgh[index][dig] is int
  Address: pgh + 20*index + 4*dig
    = pgh + 4*(5*index + dig)
int get_pgh_digit(int index, int dig)
{
return pgh[index][dig];
}
leaq (%rdi,%rdi,4), %rax # 5*index
addl %rax, %rsi # 5*index+dig
movl pgh(,%rsi,4), %eax # M[pgh + 4*(5*index+dig)]
pgh
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
pgh[1][1]

## Slide 64: Multi-Level Array Example
Variable univ denotes array of 3 elements
Each element is a pointer
  8 bytes
Each pointer points to array of int’s
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig ucb = { 9, 4, 7, 2, 0 };
#define UCOUNT 3
int *univ[UCOUNT] = {mit, cmu, ucb};
36
160
16
56
168
176
univ
cmu
mit
ucb
1
5
2
1
3
16
20
24
28
32
36
0
2
1
3
9
36
40
44
48
52
56
9
4
7
2
0
56
60
64
68
72
76

## Slide 65: Element Access in Multi-Level Array
Computation
  Element access Mem[Mem[univ+8*index]+4*digit]
  Must do two memory reads
    First get pointer to row array
    Then access element within array
salq $2, %rsi # 4*digit
addq univ(,%rdi,8), %rsi # p = univ[index] + 4*digit
movl (%rsi), %eax # return *p
ret
int get_univ_digit
(size_t index, size_t digit)
{
return univ[index][digit];
}

## Slide 66: Array Element Accesses
int get_pgh_digit
(size_t index, size_t digit)
{
return pgh[index][digit];
}
int get_univ_digit
(size_t index, size_t digit)
{
return univ[index][digit];
}
Nested array
Multi-level array
Accesses looks similar in C, but address computations very different:
Mem[pgh+20*index+4*digit]
Mem[Mem[univ+8*index]+4*digit]

## Slide 67: N X N Matrix Code
Fixed dimensions
  Know value of N at compile time
Variable dimensions, explicit indexing
  Traditional way to implement dynamic arrays
Variable dimensions, implicit indexing
  Now supported by gcc
#define N 16
typedef int fix_matrix[N][N];
/* Get element a[i][j] */
int fix_ele(fix_matrix a,
size_t i, size_t j)
{
return a[i][j];
}
#define IDX(n, i, j) ((i)*(n)+(j))
/* Get element a[i][j] */
int vec_ele(size_t n, int *a,
size_t i, size_t j)
{
return a[IDX(n,i,j)];
}
/* Get element a[i][j] */
int var_ele(size_t n, int a[n][n],
size_t i, size_t j) {
return a[i][j];
}

## Slide 68: 16 X 16 Matrix Access
/* Get element a[i][j] */
int fix_ele(fix_matrix a, size_t i, size_t j) {
return a[i][j];
}
# a in %rdi, i in %rsi, j in %rdx
salq $6, %rsi # 64*i
addq %rsi, %rdi # a + 64*i
movl (%rdi,%rdx,4), %eax # M[a + 64*i + 4*j]
ret
Array Elements
  Address A + i * (C * K) + j * K
  C = 16, K = 4

## Slide 69: n X n Matrix Access
/* Get element a[i][j] */
int var_ele(size_t n, int a[n][n], size_t i, size_t j) {
return a[i][j];
}
# n in %rdi, a in %rsi, i in %rdx, j in %rcx
imulq %rdx, %rdi # n*i
leaq (%rsi,%rdi,4), %rax # a + 4*n*i
movl (%rax,%rcx,4), %eax # a + 4*n*i + 4*j
ret
Array Elements
  Address A + i * (C * K) + j * K
  C = n, K = 4
  Must perform integer multiplication

## Slide 70: Example: Array Access
#include <stdio.h>
#define ZLEN 5
#define PCOUNT 4
typedef int zip_dig[ZLEN];
int main(int argc, char** argv) {
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
int *linear_zip = (int *) pgh;
int *zip2 = (int *) pgh[2];
int result =
pgh[0][0] +
linear_zip[7] +
*(linear_zip + 8) +
zip2[1];
printf("result: %d\n", result);
return 0;
}
linux> ./array
Notes: Stop and ask students to work out what this might print.

## Slide 71: Example: Array Access
#include <stdio.h>
#define ZLEN 5
#define PCOUNT 4
typedef int zip_dig[ZLEN];
int main(int argc, char** argv) {
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
int *linear_zip = (int *) pgh;
int *zip2 = (int *) pgh[2];
int result =
pgh[0][0] +
linear_zip[7] +
*(linear_zip + 8) +
zip2[1];
printf("result: %d\n", result);
return 0;
}
linux> ./array
result: 9

## Slide 72: Today
Arrays
  One-dimensional
  Multi-dimensional (nested)
  Multi-level
Structures
  Allocation
  Access
  Alignment
Floating Point

## Slide 73: Structure Representation
Structure represented as block of memory
  Big enough to hold all of the fields
Fields ordered according to declaration
  Even if another ordering could yield a more compact representation
Compiler determines overall size + positions of fields
  Machine-level program has no understanding of the structures in the source code
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 74: Generating Pointer to Structure Member
# r in %rdi, idx in %rsi
leaq (%rdi,%rsi,4), %rax
ret
int *get_ap
(struct rec *r, size_t idx)
{
return &r->a[idx];
}
Generating Pointer to Array Element
  Offset of each structure member determined at compile time
  Compute as r + 4*idx
r+4*idx
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 75: Following Linked List
.L11: # loop:
movslq 16(%rdi), %rax # i = M[r+16]
movl %esi, (%rdi,%rax,4) # M[r+4*i] = val
movq 24(%rdi), %rdi # r = M[r+24]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
C Code
Register | Value
%rdi | r
%rsi | val
struct rec {
int a[4];
int i;
struct rec *next;
};
Element i
r
i
next
0
16
24
32
a

## Slide 76: 不浪费存储器资源的存放方法
存储字64位（8个字节）
现有一批数据，它们依次为：字节、半字、双字、单字、半字、单字、字节、单字。4种不同长度的数据一个紧接着一个存放。
优点：不浪费宝贵的主存资源，
缺点：当访问的一个双字、单字或半字跨越两个存储单元时，存储器的工作速度降低了一半，而且读写控制比较复杂。
对齐问题

## Slide 77: 从存储字的起始位置开始存放
优点：无论访问一个字节、半字、单字或双字都可以在一个存储周期内完成，读写数据的控制比较简单。
缺点：浪费了宝贵的存储器资源。
存储字64位（8个字节）

## Slide 78: 边界对齐的数据存放方法
存储字64位（8个字节）
0
1
8
16
24
32
9
17
25
33
2
10
18
3
11
19
4
12
20
5
13
21
6
14
22
7
15
23
26
34
27
28
36
35
29
37
30
31
39
38
此方法规定，双字地址的最末3个二进制位必须为000，单字地址的最末两位必须为00，半字地址的最末一位必须为0。它能够保证无论访问双字、单字、半字或字节，都在一个存取周期内完成，尽管存储器资源仍然有浪费。

## Slide 79: Structures & Alignment
Unaligned Data
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
c
i[0]
i[1]
v
p
p+1
p+5
p+9
p+17
struct S1 {
char c;
int i[2];
double v;
} *p;

## Slide 80: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
  Required on some machines; advised on x86-64
Motivation for Aligning Data
  Memory accessed by (aligned) chunks of 4 or 8 bytes (system dependent)
    Inefficient to load or store datum that spans quad word boundaries
    Virtual memory trickier when datum spans 2 pages
Compiler
  Inserts gaps in structure to ensure correct alignment of fields

## Slide 81: Specific Cases of Alignment (x86-64)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, …
  lowest 2 bits of address must be 002
8 bytes: double, long, char *, …
  lowest 3 bits of address must be 0002
16 bytes: long double (GCC on Linux)
  lowest 4 bits of address must be 00002

## Slide 82: Satisfying Alignment with Structures
struct S1 {
char c;
int i[2];
double v;
} *p;
Within structure:
  Must satisfy each element’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example:
  K = 8, due to double element NOTE: K < sizeof(struct S1)
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
Internal padding

## Slide 83: Meeting Overall Alignment Requirement
For largest alignment requirement K
Overall structure must be multiple of K
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
Multiple of K=8
External padding

## Slide 84: Arrays of Structures
Overall structure length multiple of K
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
a+24 |  |  |  |  |  |  | a+32 |  |  |  |  |  |  |  | a+40 |  |  |  |  |  |  |  | a+48 | 
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+24 |  |  |  |  | a+48 |  |  |  |  | a+72 |  |  |  |  |  |  | 

## Slide 85: Accessing Array Elements
Compute array offset 12*idx
  sizeof(S3), including alignment spacers
Element j is at offset 8 within structure
Assembler gives offset a+8
  Resolved during linking
struct S3 {
short i;
float v;
short j;
} a[10];
short get_j(int idx)
{
return a[idx].j;
}
# %rdi = idx
leaq (%rdi,%rdi,2),%rax # 3*idx
movzwl a+8(,%rax,4),%eax
 | a[0] |  |  |  |  | • • • |  |  |  | a[idx] |  |  |  | • • |  |  | • |  |  | 
a+0 |  |  |  |  | a+12 |  |  |  | a+12*idx |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | i | 2 bytes |  | v |  |  | j | 2 bytes |  |  | 
 |  |  |  | a+12*idx |  |  |  |  |  | a+12*idx+8 |  |  |  |  | 

## Slide 86: Alignment
Structure data type
  may need to insert gaps in the field allocation
  may need to add padding to the end of the structure

## Slide 87: Simple Example
struct xxx {
int i;
char c;
double d;
};
struct xxx x[2];
0x00
0x04
0x08
0x0C
0x10
0x14
&x[0].i
&x[0].c
&x[0].d
&x[1].i
Struct整体对齐规则
由其中最大的元素决定
（此例为8字节）

## Slide 88: Complex Example
struct xxx {
short s;
char c0;
int i;
long l;
char c1;
char a[2];
double d;
char c2;
};
struct xxx x[2];
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
&x[0].s
&x[0].c0
&x[0].i
&x[0].l
&x[0].c1
&x[0].a[0]
&x[0].a[1]
&x[0].d
&x[0].c2
&x[1].s
0x20

## Slide 89: Array
struct ccc {
char c1;
char a[3];
char c2;
};
struct ccc c[2];
0x00
0x04
0x08
0x0C
0x10
0x14
&c[0].c1
&c[0].a[0]
&c[0].c2
&c[1].c1
&c[1].a[0]
&c[1].c2

## Slide 90: Array
struct ccc {
char c1;
short a[3];
char c2;
};
struct sss s[2];
0x00
0x04
0x08
0x0C
0x10
0x14
&s[0].c1
&s[0].c2
&s[0].a[0]
&s[1].c1
&s[1].c2
&s[1].a[0]

## Slide 91: Array
struct iii {
char c1;
int a[3];
char c2;
};
struct iii i[2];
0x00
0x04
0x08
0x0C
0x10
0x14
&s[0].c1
&s[0].c2
&x[0].i
&s[1].c1

## Slide 92: Saving Space
Put large data types first
Effect (largest alignment requirement K=4)
struct S4 {
char c;
int i;
char d;
} *p;
struct S5 {
int i;
char c;
char d;
} *p;
c
i
3 bytes
d
3 bytes
c
i
d
2 bytes
12 bytes
8 bytes

## Slide 93: Union
两个/多个部分，同一段内存有不同的解读方式
A single object can be referenced by using different data types
The syntax of a union declaration is identical to that for structures, but its semantics are very different
Rather than having the different fields reference different blocks of memory, they all reference the same block

## Slide 94: Union
94
struct S3 {
char c;
int i[2];
double v;
};
union U3 {
char c;
int i[2];
double v;
};
Type | c | i | v | size
S3 | 0 | 4 | 12 | 20
U3 | 0 | 0 | 0 | 8
The offsets of the fields, as well as the total size of data types S3 and U3, are:

## Slide 95: Today
Arrays
  One-dimensional
  Multi-dimensional (nested)
  Multi-level
Structures
  Allocation
  Access
  Alignment
Floating Point

## Slide 96: Background
History
  x87 FP
    Legacy, very ugly
  SSE FP
    Supported by server machines
    Special case use of vector instructions
  AVX FP
    Newest version
    Similar to SSE
    Documented in book

## Slide 97: Programming with SSE3
XMM Registers
  16 total, each 16 bytes
  16 single-byte integers
  8 16-bit integers
  4 32-bit integers
  4 single-precision floats
  2 double-precision floats
  1 single-precision float
  1 double-precision float

## Slide 98: Scalar & SIMD Operations
  Scalar Operations: Single Precision
  SIMD Operations: Single Precision
  Scalar Operations: Double Precision
+
%xmm0
%xmm1
addss %xmm0,%xmm1
+
+
+
+
%xmm0
%xmm1
addps %xmm0,%xmm1
+
%xmm0
%xmm1
addsd %xmm0,%xmm1

## Slide 99: FP Basics
Arguments passed in %xmm0, %xmm1, ...
Result returned in %xmm0
All XMM registers caller-saved
float fadd(float x, float y)
{
return x + y;
}
double dadd(double x, double y)
{
return x + y;
}
# x in %xmm0, y in %xmm1
addss %xmm1, %xmm0
ret
# x in %xmm0, y in %xmm1
addsd %xmm1, %xmm0
ret

## Slide 100: FP Memory Referencing
Integer (and pointer) arguments passed in regular registers
FP values passed in XMM registers
Different mov instructions to move between XMM registers, and between memory and XMM registers
double dincr(double *p, double v)
{
double x = *p;
*p = x + v;
return x;
}
# p in %rdi, v in %xmm0
movapd %xmm0, %xmm1 # Copy v
movsd (%rdi), %xmm0 # x = *p
addsd %xmm0, %xmm1 # t = x + v
movsd %xmm1, (%rdi) # *p = t
ret

## Slide 101: Other Aspects of FP Code
Lots of instructions
  Different operations, different formats, ...
Floating-point comparisons
  Instructions ucomiss and ucomisd
  Set condition codes ZF, PF and CF
  Zeros OF and SF
Using constant values
  Set XMM0 register to 0 with instruction xorpd %xmm0, %xmm0
  Others loaded from memory
Parity Flag
UNORDERED: ZF,PF,CF←111
GREATER_THAN: ZF,PF,CF←000
LESS_THAN: ZF,PF,CF←001
EQUAL: ZF,PF,CF←100

## Slide 102
下面的定义声明了一类结构，用来构建二叉树：
1 typedef struct ELE *tree_ptr; // 表示tree_ptr实际上是ELE*类型
2 struct ELE {
3 tree_ptr left;
4 tree_ptr right;
5 long val;
6 }
对于如下函数原型 long trace(tree_ptr tp); GCC产生了下面的x86-64代码：
1 trace: ; tp in %rdi
2 movl $0, %eax
3 testq %rdi, %rdi
4 je .L3
5 .L5
6 movq 16(%rdi), %rax
7 movq (%rdi), %rdi
8 testq %rdi, %rdi
9 jne .L5
10 .L3
11 ret ;函数返回，返回值一般放在%rax中
（1）请写出该函数的最简洁的C语言版本，使用while循环；（2）用自然语言解释该函数的功能。
Notes: Long ret = 0;
While (tp) {
ret = tp->val;
tp = tp->left;
}
Return ret;
求二叉树最左子节点的val

## Slide 103
你负责维护一个大型的C程序，遇到下面的代码：
1 typedef struct {
2 int first;
3 a_struct a[CNT];
4 int last;
5 }b_struct;
6 void test(long i, b_struct *bp) {
7 int n = bp->first + bp->last;
8 a_struct *ap = &bp->a[i];
9 ap->x[ap->idx] = n;
10}
编译时常数CNT和结构a_struct的声明是在一个你没有访问权限的文件中。幸好你有代码的.o版本，反汇编的代码为：
void test(long i, b_struct *bp) {
i in %rdi, bp in %rsi
1 000000000000 <test>:
2 0: 8b 8e 20 01 00 00 mov 0x120(%rsi), %ecx
3 6: 03 0e add (%rsi), %ecx
4 8: 48 8d 04 bf lea (%rdi, %rdi, 4), %rax
5 c: 48 8d 04 c6 lea (%rsi, %rax, 8), %rax
6 10: 48 8b 50 08 mov 0x8(%rax), %rdx
7 14: 48 63 c9 movslq %ecx, %rcx
8 17: 48 89 4c d0 10 mov %rcx, 0x10(%rax, %rdx, 8)
9 1c: c3. retq
请推断：
A. CNT的值；
B. 结构体a_struct的完整声明，假设其中只有字段idx和x，且都是有符号数
Notes: CNT=7
typedef struct {
long idx;
long x[4];
}a_struct;

## Slide 104: 课堂练习
typedef union {
struct{
short v;
short d;
int s;
} t1;
struct{
int a[2];
char *p;
} t2;
}u_type;
// 32位机环境下
//up@eax, dest@edx
void get(u_type *up, TYPE *dest) {
*dest = EXPR;
}
EXPR分为为以下值时，求TYPE和get函数的汇编代码:
1. up->t1.s
2. up->t1.v
3. &up->t1.d
4. up->t2.a
5. up->t2.a[up->t1.s]
6. *up->t2.p
Notes: 1）int, movl 4(%eax), %eax movl %eax, (%edx)
2）short, movw (%eax),%ax movw %ax, (%edx)
3）short *, leal 2(%eax), %eax movl %eax, (%edx)
4）int *, movl %eax, (%edx)
5）int, movl 4(%eax), %ecx movl (%eax, %ecx, 4), %eax movl %eax, (%edx)
6）char, movb 8(%eax), %al movb al, (%edx)

## Slide 105: 练习答案
typedef union {
struct{
short v;
short d;
int s;
} t1;
struct{
int a[2];
char *p;
} t2;
}u_type;
// 32位机环境下
//up@eax, dest@edx
void get(u_type *up, TYPE *dest) {
*dest = EXPR;
}
EXPR分为为以下值时，求TYPE和get函数的汇编代码:
1. up->t1.s
2. up->t1.v
3. &up->t1.d
4. up->t2.a
5. up->t2.a[up->t1.s]
6. *up->t2.p
1）int, movl 4(%eax), %eax movl %eax, (%edx)
2）short, movw (%eax),%ax movw %ax, (%edx)
3）short *, leal 2(%eax), %eax movl %eax, (%edx)
4）int *, movl %eax, (%edx)
5）int, movl 4(%eax), %ecx movl (%eax, %ecx, 4), %eax movl %eax, (%edx)
6）char, movb 8(%eax), %al movb al, (%edx)

## Slide 106: Summary
Arrays
  Elements packed into contiguous region of memory
  Use index arithmetic to locate individual elements
Structures
  Elements packed into single region of memory
  Access using offsets determined by compiler
  Possible require internal and external padding to ensure alignment
Combinations
  Can nest structure and array code arbitrarily
Floating Point
  Data held and operated on in XMM registers

## Slide 107: Additional Slides

## Slide 108: Understanding Pointers & Arrays #1
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] |  |  |  |  |  | 
int *A2 |  |  |  |  |  | 

## Slide 109: Understanding Pointers & Arrays #1
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] | Y | N | 12 | Y | N | 4
int *A2 | Y | N | 8 | Y | Y | 4
A1
A2
Allocated int
Unallocated pointer
Allocated pointer
Unallocated int

## Slide 110: Understanding Pointers & Arrays #2
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] |  |  |  |  |  |  |  |  | 
int *A2[3] |  |  |  |  |  |  |  |  | 
int (*A3)[3] |  |  |  |  |  |  |  |  | 
int (*A4[3]) |  |  |  |  |  |  |  |  | 

## Slide 111: Understanding Pointers & Arrays #2
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] | Y | N | 12 | Y | N | 4 | N | - | -
int *A2[3] | Y | N | 24 | Y | N | 8 | Y | Y | 4
int (*A3)[3] | Y | N | 8 | Y | Y | 12 | Y | Y | 4
int (*A4[3]) | Y | N | 24 | Y | N | 8 | Y | Y | 4
A1
A2/A4
Allocated int
Unallocated pointer
Allocated pointer
Unallocated int
A3

## Slide 112: Understanding Pointers & Arrays #3
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3][5] |  |  |  |  |  |  |  |  | 
int *A2[3][5] |  |  |  |  |  |  |  |  | 
int (*A3)[3][5] |  |  |  |  |  |  |  |  | 
int *(A4[3][5]) |  |  |  |  |  |  |  |  | 
int (*A5[3])[5] |  |  |  |  |  |  |  |  | 
Decl | ***An |  | 
 | Cmp | Bad | Size
int A1[3][5] |  |  | 
int *A2[3][5] |  |  | 
int (*A3)[3][5] |  |  | 
int *(A4[3][5]) |  |  | 
int (*A5[3])[5] |  |  | 

## Slide 113
Declaration
int A1[3][5]
int *A2[3][5]
int (*A3)[3][5]
int *(A4[3][5])
int (*A5[3])[5]
A2/A4
A5
Allocated int
Unallocated pointer
Allocated pointer
Unallocated int
Allocated pointer to unallocated int
A1
A3

## Slide 114: Understanding Pointers & Arrays #3
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3][5] | Y | N | 60 | Y | N | 20 | Y | N | 4
int *A2[3][5] | Y | N | 120 | Y | N | 40 | Y | N | 8
int (*A3)[3][5] | Y | N | 8 | Y | Y | 60 | Y | Y | 20
int *(A4[3][5]) | Y | N | 120 | Y | N | 40 | Y | N | 8
int (*A5[3])[5] | Y | N | 24 | Y | N | 8 | Y | Y | 20
Decl | ***An |  | 
 | Cmp | Bad | Size
int A1[3][5] | N | - | -
int *A2[3][5] | Y | Y | 4
int (*A3)[3][5] | Y | Y | 4
int *(A4[3][5]) | Y | Y | 4
int (*A5[3])[5] | Y | Y | 4